## Slide 1: White Matter Multi-Resolution Segmentation Using Fuzzy Set Theory
[1] S. Wakana et al., “Reproducibility of quantitative tractography methods applied to cerebral white matter”, NeuroImage, vol. 36, no. 3, pp. 630-644, 2007.
[2] I. Bloch, “Fuzzy spatial relationships for image processing and interpretation: a review”, Image and Vision Computing, vol. 23, no. 2, pp. 89-110, 2005.
[3] A. Delmonte et al., “Segmentation of White Matter Tractograms Using Fuzzy Spatial Relations”, in Organization for Human Brain Mapping (OHBM), Singapore, 2018.
[4] C. Mercier et al., “Progressive and Efficient Multi-Resolution Representations for Brain Tractograms”, in EG VCBM, 2018.
[5] P. Gori et al., “Parsimonious Approximation of Streamline Trajectories in White Matter Fiber Bundles,” IEEE TMI, vol. 35, no. 12, pp. 2609-2619, 2016.
[6] D. Wassermann et al., “The white matter query language: a novel approach for describing human white matter anatomy,” Brain Structure and Function, vol. 221, no. 9, pp. 4705-4721, 2016.
*Alessandro Delmonte1,2, *Corentin Mercier1,3, Johan Pallud4, Isabelle Bloch1,2, Pietro Gori1
1LTCI, Télécom ParisTech, Université Paris-Saclay, Paris, France
2IMAG2 Laboratory, Imagine Institute, Paris, France
3LIX, Ecole Polytechnique, Palaiseau, France
4Neurosurgery Department, Sainte-Anne Hospital, Paris, France
* equally contributed to this work
IEEE International Symposium on Biomedical Imaging – 2019 – Venice (IT)
Poster n°582
alessandro.delmonte@institutimagine.org
corentin.mercier@telecom-paristech.fr
Contacts:
INTRODUCTION / OBJECTIVE
RESULTS
SPATIAL RELATIONS MODELING
MULTI-RESOLUTION REPRESENTATION
Clinicians often describe white matter fiber bundles using spatial indication in relation to known brain references. These descriptions are intrinsically vague, thus needing an appropriate modelling framework. We apply the fuzzy set theory to represent the uncertainty of fibers to belong to a bundle, in terms of spatial, connectivity and trajectory information (e.g. anterior of Amygdala).
References
White matter fiber bundles are often described using qualitative spatial relationships (e.g. anterior of Amygdala) [1]. We propose to model their inherent vagueness using the theory of fuzzy sets [2]. Furthermore, to cope with the high redundancy of tractograms and ease interpretation, we introduce an interactive navigation and exploration technique based on a multi-resolution representation.
We validated our results on 5 unrelated healthy adults subjects from the HCP dataset.
The interactive analysis helped neurosurgeons to better understand the structure of the bundles and find an optimal ACS threshold for the segmentation of IFOF and UF.
Compared to state-of-the-art methods, a smaller fiber dispersion can be observed.
ACS thresholds were reproducible among different subjects.
We plan to extend the proposed technique to more fiber bundles, implementing more fuzzy relations, and perform statistical analyses.
FUTURE WORKS
We introduce a new term to the similarity measure (WCext) to take into account the ACS difference between two fibers X and Y, using a gaussian kernel K to regulate this effect:
We assign to every fiber an anatomical coherence score (ACS) combining, in a conjunctive way, the satisfaction degrees for all the provided descriptions. Users are able to interactively select the bundles of interest, via an ACS based thresholding operation, with the level of precision that best fit their applications.
ACS 1
ACS 2
ACS 3
IFOF
UF
0
1
ACS
Fig. 1: Fibers of interest can be selected via an ACS based thresholding operation.
FIBERS
Original Bundle
IFOF
UF
CYLINDERS
Medium Resolution
CYLINDERS
Low Resolution
ACS 1
ACS 2
ACS 1
ACS 2
0
0.8
0
1
Fig. 2: Multi-resolution fiber bundles visualization
Fig. 3: Tracts dispersion map
In order to facilitate brain navigation and to add interactivity to the segmentation process, we introduce a white matter multi-resolution representation based on [3]. Fibers are progressively merged together according to their similarity.
The interactive multi-resolution and thresholding allow for an easier understanding of the bundle as well as a better determination of the threshold at which fibers are all part of it.
https://github.com/CorentinMercier/FBTS
April 8-11, 2019
An anatomical coherence score (ACS) is assigned to each fiber combining the fuzzy spatial relations.
We propose a method for white matter segmentation exploiting spatial relations between brain regions. We model the relations inherent incertitude relying on the spatial fuzzy set theory [1,2]. To cope with the high redundancy of tractograms and ease interpretation we introduce an interactive navigation and exploration technique based on a multi-resolution brain fiber representation [3].
Compared to WMQL [4] and manual segmentation, our technique presents less scattered fibers, especially in the areas connecting the temporal and frontal lobe, as shown in the dispersion colormap of figure 3.
Bundles are defined as a logic combination of spatial (anterior of, …), connectivity (endpoint in, …) and trajectory (crossing, …) relations.
Every voxel P in the space is assigned a membership value μ describing the degree of satisfaction of the combined relations. A FS score is computed for each fiber (with endpoints f) as the weighted average of μ values of the voxels the fiber passes through.
assigns to every point P in the
space the degree of being in direction with respect to R.
Reference
Real-time and interactive:
Navigation
Multi-resolution
ACS thresholding
White matter multi-resolution [4] technique progressively merges fibers together in generalized cylinders.
Fibers are selected using an extension of the Weighted Currents [5] similarity, containing an ACS term.
with , and Ka Kb Kg being Gaussian kernels.
Real-time multi-resolution navigation
Interactive ACS thresholding for segmentation
1
0
All fuzzy spatial relations are combined in a grid containing value scores. An anatomical coherence score (ACS) is obtained for each fiber/cylinder integrating it on the grid.
An anatomical coherence score (ACS) [3] is obtained for each fiber/cylinder in a conjunctive way.
[6]
)
Connectivity:
Directional: